## Slide 1
嵌入式系統設計與實務
授課教師：逢甲大學 資訊工程系 陳德生老師、王益文老師

## Slide 2
第 13 週
PWM
- PWM, Buzzer, ADC, VR, RGBLED, LCD

## Slide 3: PWM Generators
Four PWM Generators, each generator supports
  One 8-bit prescaler and One clock divider
  Two PWM outputs, each output includes
    A 16-bit PWM down-counter
    A 16-bit PWM reload value register (CNR)
    A 16-bit PWM compare register (CMR)
  One dead-zone generator
8 PWM channels or 4 PWM paired channels
  PWM0=PA12, PWM1=PA13, PWM2=PA14, PWM3=PA15 (RGB LED : GPA12 - GPA14)
  PWM4=PB11, PWM5=PE5, PWM6=PE0, PWM6=PE1
PWM Interrupt synchronized with PWM period
Single-shot or Continuous mode

## Slide 4: PWM Frequency & Duty Cycle
PWM Frequency = PWM_CLK/(prescale+1)*(clock divider)/(CNR+1);
Duty ratio = (CMR+1)/(CNR+1)
CMR+1 >= CNR: PWM output high.
CMR+1 < CNR: PWM output low

## Slide 5
3
Keil Demo
PWM Frequency
Buzzer

## Slide 6: C Codes : Buzzer (GPB11) = PWM4
6
int32_t main()
{
SYS_Init();
  PWM_EnableOutput(PWM1, PWM_CH_0_MASK);
  PWM_Start(PWM1, PWM_CH_0_MASK);
  for (i=0; i<72; i++) {
  PWM_ConfigOutputChannel(PWM1, PWM_CH0, music[i], 90); if (music[i]!=0) PWM_EnableOutput(PWM1, PWM_CH_0_MASK);
  else PWM_DisableOutput(PWM1, PWM_CH_0_MASK);
  CLK_SysTickDelay(pitch[i]);
  }
}
PWM Frequency = music[i]

## Slide 7
3
Keil Demo
PWM Duty Cycle
ADC(VR1)
RGBLED

## Slide 8: C Codes : RGB LED (GPA12,GPA13, GPA14)
8
int32_t main()
{
//initialize SYS, ADC, and PWM
print_Line(0, "VR1 connect ADC7");
while(1){
ADC_START_CONV(ADC);
  u32ADCvalue = ADC_GET_CONVERSION_DATA(ADC, 7);
duty = u32ADCvalue*100/4096;
  PWM_ConfigOutputChannel(PWM0, PWM_CH0, 60, duty);
  PWM_ConfigOutputChannel(PWM0, PWM_CH1, 60, duty);
  ADC_DisableInt(ADC, ADC_ADF_INT);
}
void Init_ADC(void)
void Init_PWM (void)
void ADC_IRQHandler(void)

## Slide 9: Practice VR1 connect ADC7 (GPA7)

## Slide 10
3
Keil Demo
PWM Frequency
ADC(VR1)
Buzzer
LCD

## Slide 11: C Codes : PWM Frequency, ADC(VR1), Buzzer, LCD
11
int32_t main()
{
//initialize SYS, ADC, and PWM
print_Line(0, "VR1 connect ADC7");
while(1){
ADC_START_CONV(ADC);
  u32ADCvalue = ADC_GET_CONVERSION_DATA(ADC, 7);
  //convert binary codes to asscii codes for LCD dsiplay
  PWM_ConfigOutputChannel(PWM1, PWM_CH0, u32ADCvalue, 90);
  ADC_DisableInt(ADC, ADC_ADF_INT);
}
void Init_ADC(void)
void Init_PWM (void)
void ADC_IRQHandler(void)

## Slide 12
Practice PWM Frequency, ADC(VR1), Buzzer, LCD
VR1 connect ADC7
VR1 = 0.982V
frq = 1219Hz

## Slide 13
版權聲明
素材內容 | 引用來源 | 授權說明
PPT | https://drive.google.com/drive/folders/1dwAL_a18o_VV9iBkfLwzhcTKHnRy5K9S?usp=sharing 郭子仁 MCU Interfaces & Driver Design 2020 | 

## Slide 14
有著作權，侵害必究©逢甲大學
Copyright@Feng Chia University