## Slide 1
嵌入式系統設計與實務
授課教師：逢甲大學 資訊工程系 陳德生老師、王益文老師

## Slide 2
第 13 週
ADC
- VR, ADC & LCD

## Slide 3: ADC specification
Analog input voltage range: 0~Vref= 3.3V
12-bit SAR ADC (10-bit accuracy)
Input channel:
  Up to 8 single-end analog input channels ADC0 ~ ADC7 = PA0 ~ PA7
  4 pairs of differential analog input channel.
Up to 800KSPS
The maximum ADC operating frequency is 16M Hz
Three ADC operation modes
  Single mode
  Single-cycle mode
  Continuous mode
Decimal | Binary | Voltage (Vref=3.3V)
0 | 0000_0000_0000 | 0/4096 * 3.3V
1 | 0000_0000_0001 | 1/4096 * 3.3V
2048 | 1000_0000_0000 | 2048/4096 * 3.3V
4095 | 1111_1111_1111 | 4095/4096 * 3.3V

## Slide 4: SAR (Successive Approximation Register) ADC
SAR
DAC
Comparator
clock
Vref
End-Of-Conversion
Vin
Sample
& Hold
-
+
N-bit

## Slide 5: ADC Single mode

## Slide 6: ADC Single-Cycle mode

## Slide 7: ADC Continuous mode

## Slide 8: C Codes :
8
int32_t main()
{
//initialization
print_Line(0, "VR1 connect ADC7");
while(1){
u32ADCvalue = ADC_GET_CONVERSION_DATA(ADC, 7);
//convert ADC output binary code to ASSCII codes
//display ASSCII codes on LCD
}
void Init_ADC(void)
void ADC_IRQHandler(void)

## Slide 9
3
Keil Demo
ADC VR1 & LCD

## Slide 10: Practice VR1 connect ADC7 (GPA7)
VR1 connect ADC7
0.663V

## Slide 11
版權聲明
素材內容 | 引用來源 | 授權說明
PPT | https://drive.google.com/drive/folders/1dwAL_a18o_VV9iBkfLwzhcTKHnRy5K9S?usp=sharing 郭子仁 MCU Interfaces & Driver Design 2020 | 

## Slide 12
有著作權，侵害必究©逢甲大學
Copyright@Feng Chia University